密码感应卡独立式门锁

Password induction card independent type door lock

版本：V1.0

密码加Mifare卡办公室、家用智能安全门锁是IC一卡通系统组成部分之一，其使用的Mifare卡可以用在其他一卡通设备上。The password and Mifare card office, household intelligent safety door lock IC card system is part of the use of the Mifare card can be used in other one-card equipment.

本门锁系统功能强大，使用灵活方便，可实现一卡多门、一门多卡的开门方式，并可将门锁设置成常开状态，房门假锁（门没有锁好）时，门锁会自动报警提示。密码、开门卡全部由用户自己删除和配制，最大限度地减少安全漏洞。本系统采用Mifare卡，是一种普及型感应卡（如小区停车场等）。本门锁适用于现代化办公室、写字楼，高级小区公寓、别墅等。Mifare卡密码办公室、家用门锁系统有以下两种开门模式：

This door lock system powerful, flexible and convenient use,  can realize a card, more than a door open the door way of card, and can be set to the door lock to often open position, the door false lock (the door is locked), door locks will automatically alarm prompt. The password, open the door all card by users themselves delete and configuration, minimize security vulnerabilities. The system USES the Mifare card, is a kind of affordable induction card (such as village parking lot, etc.). This door lock is applicable to modern office, office buildings, senior residential apartments, villas and so on. Mifare card password office, home door lock system has the following two kind of open mode:

独立式：单独使用Mifare卡或密码可以开门。

Ø independent type: used alone Mifare card or password can open the door.

组合式：Mifare卡和密码同时使用才可以开门。

Ø combined-type: Mifare card and password use at the same time can open the door.

注：

Note:

1.本系统的门锁出厂初始化后的管理密码为12345678，开门模式为独立式。

1. This system lock factory is initialized management password for 12345678, open the door model of independent type.

  - 从独立式切换到组合式操作如下：

1.1. From independent type switch to the combined operation as follows:

输入8位管理密码按钥匙键后再按6#键蜂鸣器长鸣5声，红蓝灯闪烁，再按钥匙键确认，蜂鸣器“嘀”长响一声，切换成功。若退出则按C号键; Input eight management according to the key password button again to 6 # key keep buzzer 5 sound, red blue lights flashing, then press the key key confirmation, a buzzer "di" with a long ring, switch success. If exit is based on C number keys;

1.2.从组合式切换到独立式操作如下：From combined-type switch to independent type operation as follows:

刷管理卡后输入8位管理密码按钥匙键，再按6#键蜂鸣器长鸣5声，红蓝灯闪烁，再按钥匙键确认，蜂鸣器“嘀”长响一声，切换成功。若退出则按C号键; Brush after eight card input password management according to the key key, then press the # 6 key keep buzzer 5 sound, red blue lights flashing, then press the key key confirmation, a buzzer "di" with a long ring, switch success. If exit is based on C number keys;

2.在组合模式下，若先读卡（或先输入密码后按钥匙键）则“嘀”一声指示灯蓝灯闪烁，然后输入开门密码按钥匙键（或读卡）蓝灯亮开门。

2. In combination mode, if you read the card (or enter the password and press the key key), "di" with a blue lights flashing lights, then open the door to the input password by key key (or reading card) blue light to open the door.

Mifare卡锁的操作指南Mifare card lock operation guideline

⑴ 管理卡 The   management  card

功能：设置和删除有效开门卡；可以开门。

Function: set and delete effective open the door card; Can open the door.

⑵ 开门卡Open the door card

功能：开门及设置通道锁

Function: open the door and lock setting channel

- 机械钥匙mechanical key

功能：紧急开门、配管理卡。

Function: open the door, with an emergency card

- 设置管理卡、删除管理卡Card, delete set card

1．1在门锁初始化（按PCB板开关约3秒后长鸣一声，松开手指，绿灯快闪进入配管理卡状态，此时读的卡即为管理卡，成功蜂鸣器“嘀”长响一声。同时注销原来的管理卡。最多可以设主控卡2张。

1 in the door lock initialization (in PCB about 3 seconds after switch keep a sound, loosen the fingers, a green light flash card, with state at this time to read card namely card for success, "di" long buzzer rang 1. At the same time the cancellation of the original. Most card may have master card 2 copies.

1．.2用机械匙开门，并保持机械匙在开锁状态约3秒后长鸣一声，绿灯快闪进入配管理卡状态（开锁状态是指锁芯的斜舌和大方舌都缩入锁体内），松开机械匙，此时读卡即为管理卡，成功蜂鸣器“嘀”长响一声，同时注销原来的管理卡。最多可以设主控卡2张。Using a mechanical key to open the door, and keep the key in the lock mechanical state about 3 seconds later with a keep, a green light flash into card with state (the lock state refers to the lock core inclined tongue and generous tongue are shrinking into the lock body), and loosen the mechanical key, this time the reading card namely card for, buzzer success "di" with a long ring, at the same time, the cancellation of the original card. Most may have 2 of master card.

- 配开门卡Open card with

2．1进入配匙状态Into key state with

读管理卡，蜂鸣器“嘀”的响一声，电机转动，蓝灯闪烁，此时可以开门，开门后灯灭。若没有开门就进入配匙状态，此时读的卡即为开门卡。5秒内门锁如果没有检测到有效的IC卡，则蜂鸣器“嘀、嘀”两声短鸣，配匙结束。Read the card, a buzzer rang "di" of a sound, motor rotation, blue lights flashing, this time can open the door, open the door back out. If there is no open the door into the state with key, and at the time that read card for open the door card. 5 seconds if no effective detection to lock the IC card, then a buzzer "di, di" with two short sound, match spoon ended.

2．2配匙操作过程With key operation process

进入配匙状态后，用IC卡接近门锁的感应区，配匙成功蜂鸣器“嘀”长响一声。重复此操作可以配其它的开门卡。如果此卡已经存在，则蜂鸣器发出“嘀嘀”的2声短鸣。最多可以配200张卡。Spoon into the match after state, close to the door lock by IC card inductive zone, deserve success spoon buzzer "di" with a long ring. Repeat this operation can be equipped with other open the door card. If this card exists already, it is a buzzer send out "di di" with two short noisily. Most can be equipped with 200 card.

- 删除开门匙Delete key to open the doo

3．1 删除单个开门卡Delete the single open the door card

把管理卡靠近感应区读两次，则蜂鸣器发出“嘀”的一声长鸣，红灯闪烁，把要删除的开门卡靠近感应区读一次，‘嘀’一声短鸣，表示该卡已经被删除。重复此操作可以删除其它的开门卡。如果此卡不存在，则蜂鸣器发出“嘀嘀”2声短鸣。The inductive zone card close to read two times, is a buzzer "di" keep a sound, the lights flashing, trying to remove the card inductive zone close to open the door to read a times, ' 'a loud sound di short, says card has been deleted. Repeat this operation can delete other open the door card. If this card does not exist, then a buzzer send out "di di" with two short noisily.

3．2删除单个遗失开门卡Delete a single card lost to open the door

把管理卡靠近感应区读三次，则蜂鸣器发出“嘀、嘀”的两声长鸣，红灯闪烁，把遗失卡的前一张开门卡靠近感应区读一次，‘嘀’一声短鸣，表示该遗失卡已经被删除。如果是第一张开门卡遗失，则在此壮态下读最后的一张开门卡。The inductive zone card close to read three times, is a buzzer "di, di" of two keep sound, the lights flashing, lost card open the door before a card inductive zone close to read a time, "di" with a short Ming, said the lost card has been deleted. If is the first piece of open the door card is lost, the strong condition in the read one of the last open card.

3．3 删除所有开门卡Delete all open the door card

把管理卡靠近感应区读五次，则蜂鸣器发出“嘀、嘀、嘀”的三声长鸣，红灯闪烁，最后‘嘀、嘀’两声，删除完成，即注销原来所有的开门卡。原有效开门卡不能再开锁，只有通过主控匙重新配匙后方可开锁。The inductive zone card close to read five times, is a buzzer tick, tick, tick "keep three, the lights flashing, finally 'di, di' two sound, delete complete, that is, the cancellation of the original of all open card. The original effective card can't open the door lock, only through the master key to match the key in the lock.

注：添加新的开门卡总是从最前面删除卡的位置往后排。

Note: add new open the door to the front of the card from always delete the position of the card to the back row

- 开门open the door

4．1 IC卡匙开门IC card key to open the door

用有效的IC卡接近门锁的感应区，蜂鸣器“嘀”的一声，马达动作，蓝灯亮，提示锁已开。门锁检测到开门动作后，自动锁门；如果没有检测到开门动作，5秒钟后，绿灯灭，也自动锁门。

With effective IC card close to the door lock inductive zone, a buzzer "di" the sound, the motor action, blue light, indicating that the lock have already opened. Open the door to door locks detection moves, automatic lock the door; If no detection to open the door to the movement, the five (5) seconds, a green light out, also automatically to lock the door.

注：

Note：

- 如果IC卡不是有效的开门匙，则“嘀、嘀、嘀”的三声短鸣，红灯亮。

② 如果电压不足，则蜂鸣器“嘀、嘀、嘀、嘀、嘀”连响五声，红灯亮。第一次低电压提示后，仍可以开门200次以上，为了保证门锁的正常使用，应及时更换电池。

(1) if the IC card is not a valid key to open the door, the "tick, tick, tick" three short sound, the red light.

(2) if the voltage is insufficient, the buzzer "tick, tick, tick, tick, tick" even five rings, the red light. The first low voltage prompted, still can open the door over 200 times, in order to ensure the normal use of door lock, should be to replace the battery.

4．2机械钥匙开门Mechanical key in the

在任何情况下（如电池压不足）都可用机械钥匙开锁。In any case (such as the insufficient battery) can be used mechanical key in the lock.

- 关门报警提示close the door alarm prompt

5．1门没有锁上报警The door is locked alarm

当门关上但斜舌没有出来或只出来一部分，俗称“假锁”时， 门锁会发出1分种的警报声以及红灯闪烁，重新锁好后警报停止。When the door is closed but the tongue no out or just part of out, commonly known as the "false" lock, door locks will issue 1 minutes alarm and the lights flashing, lock again after warning to stop.

- 常开（通道）设置often a set

6．1通道设置：

Channel Settings:

按住后把手，把锁舌收回来，保持不动，刷开门卡或者管理卡，蜂鸣器长叫一声，红灯闪1下，马达开门动作，门处于常开（通道状态）。After holding his hand, lock tongue back, to keep still, brush card or open card, called a loud buzzer long, red light flash 1, open the door to the motor movement, the door is often a (channel state).

6．2解除通道状态：

Remove channel state:

按住后把手，把锁舌收回来，保持不动，刷开门卡或者管理卡，蜂鸣器短叫一声，绿灯闪1下，马达关门动作，门锁上（解除通道状态）。After holding his hand, lock tongue back, to keep still, brush card or open card, called a loud buzzer short, a green light flash 1, motor closed action, lock the door (remove channel state).

注：当门锁处于常开状态时，用开门卡开门，“嘀”1声短声，然后亮红灯。但门锁电机不会动作，因为此时门已处于常开状态。

Note: when the door lock is often a state, open the door open with the card, "di" 1 sound short sound, then the red light. But lock motor won't action, because the door already is often a state.

密码锁的操作指南

⑴ 管理密码Management password

功能：设置和删除有效开门密码并可开门。Function: set and delete effective password and can open the door to open the door.

⑵ 开门密码Open the door the password

功能：开门Function: open the door

- 更改管理密码Change management password、

1．1输入原8位密码后按1号键蜂鸣器长鸣一声，红蓝灯闪烁，此时输入新的密码后按钥匙键蜂鸣器长鸣一声确认后再次输入密码后按钥匙键蓝灯亮，蜂鸣器长鸣二声则管理密码修改成功。如第二次输入密码错误按钥匙键后蜂鸣器“嘀、嘀、嘀、嘀、嘀”5声后重新输入。若退出则按*号键。Input the original eight password and press 1 with a key keep buzzer, red blue lights flashing, this time the new password input according to keep a loud buzzer key key confirm password again after blue light in key key, keep buzzer two sound is management password changing success. Such as the second input password mistake by key key buzzer "tick, tick, tick, tick, tick" 5 empress enter again. If exit then the * key.

1.2用机械匙开门，并保持机械匙在开锁状态约3秒（开锁状态是指锁芯的斜舌和大方舌都缩入锁体内），蜂鸣器“嘀”的长响一声、红蓝灯闪烁，松开钥匙，此时输入8位密码后按钥匙键蜂鸣器长鸣一声确认后再次输入密码后按钥匙键蓝灯亮，蜂鸣器“嘀、嘀”长响二声，则此密码为新的管理密码。Using a mechanical key to open the door, and keep the key in the lock mechanical state about 3 seconds (lock state is to point to lock core inclined tongue and generous tongue are shrinking into the lock body), a buzzer "di" with a long ring, red blue lights flashing, loosen the key, this time the input eight password key key keep buzzer according to confirm a sound again after the input password and press the key key blue light, a buzzer "di, di" long ring two sound, then the password for the new management password.

- 配开门密码Open the door, with a password

输入8位管理密码按钥匙键后再按8号键蜂鸣器长鸣一声，蓝灯闪烁，此时输入6位密码后按钥匙键蜂鸣器长鸣一声确认后再次输入刚输的密码后按钥匙键蓝灯亮，蜂鸣器长鸣两声则开门密码设置成功。如第二次输入密码错误则按钥匙键蜂鸣器“嘀、嘀、嘀、嘀、嘀”5声后重新输入。重复此操作可以配其它的开门密码。如果此密码已经存在，则蜂鸣器发出“嘀嘀嘀”的三声短鸣。最多可以配50个开门密码。若退出则按*号键。Input eight management according to the key again after key password by 8 key keep buzzer a sound, blue lights flashing, this time the input six password and press keys with a key keep buzzer confirmed input again just lost password and press the key key blue lights up, keep buzzer two sound is open the door password success. Such as the second input password mistake then the buzzer key key tick, tick, tick, tick, tick "5 empress enter again. Repeat this operation can be equipped with other open the door the password. If this password exists already, it is a buzzer send out "di di di" of three short noisily. Most can be equipped with 50 open the door the password. If exit then the * key.

- 删除或修改开门密码delete or modify open the door the password

3．1删除单个开门密码Delete the single open the door the password

输入8位管理密码后按4号键蜂鸣器长鸣一声，红灯闪烁，输入要删除该密码的前一组开门密码，‘嘀’一声短鸣，删除成功。如果要删除第一组开门密码，则在此壮态下输入最后的一组开门密码。若退出则按*号键。Input eight management password 4 key according to keep buzzer 1, the lights flashing, input to delete the password ago a group of open the door the password, "di" with a short sound, delete success. If you want to delete the first group password to open the door, the strong condition in this next input the final group of open the door the password. If exit then the * key.

3．2 删除所有开门密码Delete all the password to open the door

输入8位管理密码后按0号键蜂鸣器长鸣一声，红灯快速闪烁后再按钥匙键确认则蜂鸣器发出“嘀、嘀、嘀”的三声长鸣，红蓝灯闪烁，最后‘嘀、嘀’两声，删除完成，即注销原来所有的开门密码。若退出则按*号键。Input eight management password, according to 0 key keep buzzer a sound and rapid flashes red light after press again confirm is a key key buzzer tick, tick, tick "keep three, red blue lights flashing, finally 'di, di' two sound, delete complete, that is, the cancellation of the original all open the door the password. If exit then the * key.

3．3修改开门密码Modify open the door the password

输入原6位开门密码后按1号键蜂鸣器长鸣一声，红蓝灯闪烁，此时输入新的6位密码后按钥匙键蜂鸣器长鸣一声确认后再次输入密码后按钥匙键蓝灯亮，蜂鸣器长鸣三声则开门密码修改成功，原开门密码失效。如第二次输入密码错误则按钥匙键蜂鸣器“嘀、嘀、嘀、”嘀、嘀5声后重新输入。若退出则按*号键。Input the original six open the door the password and press 1 with a key keep buzzer, red blue lights flashing, this time the input new six password and press keys with a key keep buzzer confirm password again after blue light in key key, keep buzzer three is open the door password changing success, the original open the door the password expiration. Such as the second input password mistake then the key key buzzer "tick, tick, tick," di, di five empress enter again. If exit then the * key.

注：添加新的开门密码总是从最前面删除密码的位置往后排。

Note: add new password from the front is always open to delete the position of the password to the back row.

- 开门open the door

4．1 管理密码开门Management password to open the door

输入管理密码后按钥匙键，蜂鸣器“嘀”一声，马达动作，蓝灯亮，提示锁已开。门锁检测到开门动作后，自动锁门；如果没有检测到开门动作，5秒钟后，蓝灯灭，也自动锁门。Input password management according to the key after key, a buzzer "di" 1, motor action, blue light, indicating that the lock have already opened. Open the door to door locks detection moves, automatic lock the door; If no detection to open the door action, 5 seconds later, blue lamp, also automatically to lock the door.

4．2开门密码开门Password to open the door to open the door

输入开门密码后按钥匙键，蜂鸣器“嘀”一声，马达动作，蓝灯亮，提示锁已开。门锁检测到开门动作后，自动锁门；如果没有检测到开门动作，5秒钟后，蓝灯灭，也自动锁门。The key to open the door to the input password key, a buzzer "di" 1, motor action, blue light, indicating that the lock have already opened. Open the door to door locks detection moves, automatic lock the door; If no detection to open the door action, 5 seconds later, blue lamp, also automatically to lock the door.

注：连续5次输入错误密码锁键盘5分钟

如果是无效的密码，则蜂鸣器发出“嘀、嘀、嘀”的三声短鸣，红灯亮。

如果电压不足，则蜂鸣器“嘀、嘀、嘀、嘀、嘀”连响五声，红灯亮。第一次低电压提示后，仍可以开门200次以上，为了保证门锁的正常使用，应及时更换电池

Note：  5 times in a row keyboard input errors combination lock for 5 minutes

If is invalid password, is a buzzer tick, tick, tick "three short sound, the red light.

If the voltage is insufficient, the buzzer "tick, tick, tick, tick, tick" even five rings, the red light. The first low voltage prompted, still can open the door over 200 times, in order to ensure the normal use of door lock, should be to replace the battery

- 特别提示Special hints

5．1为了你的财产安全，我们在此特别提醒您门锁安装完成后请立即修改管理码并删除所有开门密码

5.1 for the sake of you of the property security, we in this special remind you lock installation is completed please immediately revision management code and delete all the password to open the door

5．2为了提高安全性，本系统支持开门乱码功能。比如：正确的密码为123456，可以在此密码的前、后任意增加数字（密码最多不超过12位），如012123456798

5.2 in order to improve security, this system support open the door garbled function. For example: the correct password for 123456, can in this password before and after the increase of any digital (password not more than 12 of the most), such as 012123456798

5．3机械钥匙是设置管理卡和管理密码的关键，又可以应急开锁，我们建议须由专人负责妥善保管。

5.3 mechanical key card and password management is to set the key, and can emergency unlock, we suggest that should be made by the specialist is responsible for safe keeping.

主要功能特点：

The main function characteristics:

- 卡片类型: Mifare感应卡

card types: Mifare induction card

- 触摸按键密码输入

touch-key password input

- 微波方式检测卡片靠近

microwave way detection CARDS close to

- 开锁方式可自行设置：Mifare卡和密码可独立开锁/Mifare卡和密码同时使用才能开锁

lock mode can set: Mifare card and password can be independent Mifare card and password lock/unlock can use at the same time

- 卡片在锁上设定，无需系统软件，最多可设2张管理卡，200张开门卡

card in the lock setting, no system software, set up to 2 pieces of card, 200 zhang open the door card

- 密码可自行修改，最多可设一个管理密码，50个开门密码

card in the lock setting, no system software, set up to 2 pieces of card, 200 zhang open the door card

- 密码支持乱码输入，最长可输入12位

password support garbled input, the longest can enter 12 a

- 可设置通道

can be set to channel

- 门“假锁”报警

door "false" lock alarm

- 低压报警提示

low voltage alarm prompt

- 电池供电，可外接应急电源

battery power supply can be external emergency power

主要技术指标：

The main technical indexes

1工作电压: 6.0V（4节碱性电池）  working voltage: 6.0 V (section 4 alkaline batteries)

2静态功耗: ＜100uA   static power consumption: < 100 uA

3 动态功耗: ＜200mA   dynamic power consumption: < 200 mA

4 电池寿命: 10个月以上（4节5#正品碱性电池）  battery life: 10 months above (section 4 # 5 folds of the alkaline batteries)

5 低电压提示: 4.5V   low voltage tip: 4.5 V

6 读卡距离: >25mm   reading card distance: > 25 mm

7 工作温度: 0℃—70℃  working temperature: 0 ℃-70 ℃

8  工作湿度: ≤80%  work humidity: more than 80%